## Slide 2
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 3
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 4
+
Wide range: an answer adapted to each needs
WC Range
OPERA
VEXTRA
DYNACIAT
HYDROCIAT
DYNACIATPOWER
kW
30
90
200
500
700
1000
20
HYDROCIATTURBO
1700

## Slide 5
11 sizes of water / water chiller and heat pump
LG Cooling capacity from 200 to 700 kW
LG Heating capacity from 250 to 820 kW
3 ACOUSTICS VERSIONS
STD – LN - XLN

## Slide 6
The range
1400V
1600V
700V
800V
900V
1000V
1100V
1200V
1800V
2100V
2400V
2 refrigerant circuits

## Slide 7
The range
Chart: 
| 700V | 800V | 9000V | 1000V | 1100V | 1200V | 1400V | 1600V | 1800V | 2100V | 2400V
Cooling | 203 | 242 | 278 | 320 | 348 | 382 | 439 | 495 | 574 | 651 | 703
Chilled water = 12°C / 7°C Hot water = 30°C / 35°C
Cooing cap.
Pf kW

## Slide 8
The range
Hot water = 40°C / 45°C Chilled water inlet = 10°C with same water flow than cooling mode
Pc kW
Heat
pump

## Slide 9
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 10
Design
STANDARD VERSION
LN – XLN VERSIONS
Notes: La filosofía modular de este equipo puede verse claramente en la construcción del mismo en función de la potencia frigorífica que se necesita. Básicamente, cada módulo es una batería en V que ocupa menos espacio con esta disposición. Según aumentamos la potencia, vamos aumentando el número de módulos respetando siempre una construcción de tipo túnel.
Como podemos observar en el dibujo la filosofía que se sigue es la de tener un equipo abierto por los dos laterales para tener acceso fácil y rápido a todos los componentes.
El grupo hidraúlico se situaría en uno de los extremos del equipo y en el opuesto se encuentra el cuadro eléctrico.

## Slide 11
Design
Modèles | Pf kW | Dimensions (mm) |  | 
 |  | L | P | H
700V à 1200V | 218 à 386 | 2099 | 996 | 1869
1400V à 1600V | 444 à 500 | 2499 |  | 1970
1800V à 2400V | 584 à 716 | 3350 |  | 
H
L
W
Compact units
up to 200 kW / m2

## Slide 12
Design
990 mm
Foot print reduced
40% to 50% vs Screw Solution
Easy integration in all
technical rooms

## Slide 13
DYNACIATPOWER foot print is similar than competition
Benchmark Foot Print

## Slide 14
=
Latest generation of scroll compressors
2 refrigerant circuits brazed plates evaporator
2 refrigerant circuits brazed plates condenser
Components
CIAT Controller CONNECT2

## Slide 15
Brazed plates heat exchanger
Maximum cooling capacity in a minimum place
Reduction of refrigerant charge
High efficiency vs shell and tubes
Plates in stainless stell 316L
VICTAULIC connection
Water differential pressure switch mounted
ARMAFLEX thermal insulation

## Slide 16
FUNCTIONAL DRAWING
COOLING WITH DRY-COOLER

## Slide 17
FUNCTIONAL DRAWING
HEATING/COOLING HYDRAULIC INVERSION
COOLING OPERATION

## Slide 18
HEATING OPERATION
FUNCTIONAL DRAWING
HEATING/COOLING HYDRAULIC INVERSION

## Slide 19
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 20
EER
COP
FULL LOAD PERFORMANCES
Do not focus on the EER It accounts for only 3% of the annual power consumption
In HVAC let us focus on the annual energy efficiency SEER & SCOP
In Process let us focus on SEPR

## Slide 21
SCROLL technology Seasonal optimization
Seasonal thermal load
Only
3 months
above 75%

## Slide 22
COMFORT SEER
PROCESS SEPR
PROCESST N° 2015/1095 ENTR Lot 1
<300 = 3.29 >300 = 4.37
Up to 400kW DYP LG is efficient as a screw solutions
ECODESIGN 2021 SEER up to 400kW
 ECODESIGN Process SEPR
SEASONAL PERFORMANCES – Part Load

## Slide 23
SEASONAL PERFORMANCES – Part Load
Bellow 400kW performances similar to competition
COMFORT SEER
No Scroll offer SEER compliance > 400kW
Units > 400kW sales as HP (SCOP)

## Slide 24
SCOP
SEASONAL PERFORMANCES – Part Load
No datas from competition over 400kW
(Ecodesign limit for HP)

## Slide 25
ECODESIGN COMPLIANCE
Compliance SCOP & SEPR-8°C
= Conformity = CE mark

## Slide 26
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 27
Condenser water outlet °C
Evaporator water outlet °C
Running limit
30
5
-12
55
18
GLYCOL OBLIGATOIRE
FULL LOAD
GLYCOL WATER
FULL LOAD
PURE WATER
-4
45
PART LOAD OPERATION

## Slide 28
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 29
3 versions
Standard
Low Noise
Xtra Low Noise
Sound level
Casing only (LN)
Casing + phonic insulation (XLN)

## Slide 30
Acoustic Performance
Standard version of DYNACIATPOWER is quieter than a screw solution
LN = -4 dB(A)
XLN = -9 dB(A)

## Slide 31
Acoustic Performance
DYNACIATPOWER a quiet solution vs competition

## Slide 32
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 33
Accessibility
Compressors
access
Electrical panel access
Exchangers
access
Sight glass, expansion valve, filter drier access
Easy access for
all the components
Easy maintenance

## Slide 34
Hydraulics connections
One
evaporator
One
condenser
Easy hydraulic connections

## Slide 35
CIAT exchanger
Victaulic in standard
Victaulic-flange adapter (option)+ connection sleeve (option)
Water filter (option)
Hydraulics connections
Item | Description
1 | Victaulic clamp
2 | Flange connection
5 | Anti-vibration sleeve
Filter
1
2
5
Complete components
for easy installation

## Slide 36
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 37
Controller
A control for all running conditions
  Chilled water inlet or outlet control
  Control according to external temperature
  Low temperature ice storage control
  Two set points management

## Slide 38
LCD 4 lines of 24 characters multilingual (F-GB-D-SP-NL-ITA-RUS)
Running and fault parameter management
Pressures and temperatures reading
Compressors starting and running time management
Compressors anti-short cycle
Pump management – Stand by function
Fault memory 20 faults memory
Master/slave function for two units
Hourly programming
Password access (3 levels)
Controller

## Slide 39
Ergonomic display
Controller
On / Off
Voltage indication
Set point 1/2 selection
Circuit fault
Reset
Escape
Validation
General fault
LCD screen
Heating/Cooling selection

## Slide 40
Available free voltage contacts inputs :
  Unit and pump ON/OFF contact
  Compressor load shedding
  Set point 1/2 selection
  HEATING / COOLING mode selection
  Set point control by 4-20mA SIGNAL
Available free voltage contacts outputs :
  General fault of the unit
  Pump control
Controller

## Slide 41
230 V-1Ph-50Hz
Free contact relay card
  Water flow fault
  Antifreeze fault
  HP and LP fault
  Compressors stage fault
  Fans fault (air / water unit)
  Discharge temperature fault
  Compressors stage status
RS 485 (2 shielded wires)
1000 meters maxi
Communication

## Slide 42
Sortie RS 485 MODBUS-JBUS (standard) / MODBUS TCP – Ethernet
BACNET & LON (option)
HYSYS Easy & Smart CIATControl
POLE ENERGY Power’Control – Cristo’Control
Free voltage contacts relay card (option)
Master/Slave
Communication
ABOUND HVAC
Performance
& Connect service

## Slide 43: Design example with Easy CIATControl 120
Boiler
Air extractor
ON / OFF control of 8 equipments
Max. 60 FCUs with V3000 on one KNX line
1 chiller
Easy CIATControl 120
Max. 4 Floways
Max. 60 FCUs with V3000 on one KNX line
Ethernet line
External BMS BACnet or OPC
Remote access

## Slide 44: Easy CIATControl with several energy producers
Master / Slave function

## Slide 45
SYNOPTIQUE
CURVES
EVENTS
PARAMETERS
REPORTS
INFORMATIONS
delivered as accessories by ERCD
45

## Slide 46
Synoptic
Trends
Events
Parameters
Information
Reports
Visualize the synoptic of the installation in real time, the status of each component, the temperatures, pressures, flows, operating mode,…
Visualize the predefined trends or design your own trends (temperatures, pressures, modes, status,…)
Visualize the list of events and the context of each event (status of the installation when the fault appears)
Set all the parameters as easily as you are in front of the system
All parameters are order by categories for an easy use.
See all details you need about the installation, the machine, the modem, the contract…
Generate reports and visualize the efficiency of your installation, and optimize your system
Easy Service Maintenance

## Slide 47
Trend
Operating times
Number of compressor starts
Event reports
Preventative maintenance actions
Energy consumption (Electricity metering)
Content
Monthly
Available on dedicated website
Range
Annual
Sent by CIAT team
On demand
Sent by CIAT team
Reports
Added Value
Expert analysis
Actionable reports

## Slide 48
Equipment availability
CIAT
Expertise
Better
profitability
Added-value
services
Real-time
data
Energy
performance
Steady
indoor air quality
Equipment optimal
control
Expertise and Analysis
ABOUND HVAC Performances

## Slide 49
Users needs
AEROCONNECT Offre System

## Slide 50
RS 485 (2 shielded wires )
1000 m Maxi
+
Signal 0-10V
Aéroconnect
  Card integrated into the dry cooler electrical panel
  Communication between chiller and dry cooler
  Chiller + dry cooler operation optimization

## Slide 51
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 52
Standard equipments
Water flow switch (differential pressure switch)
Compressors mounted on anti vibration mounts
Main safety switch
Auxiliary transformer
RS485-TC/IP for BMS connection on open protocol Modbus-Jbus
Electrical panel Wiring numbering
Electrical components marking
Compressor discharge valve (1 per circuit)
Master / slave management for two units
Electronic expansion valves (sizes 1800V to 2400V)
Stand by pump function
Low temperature glycol water (-12°C)

## Slide 53
Options
Low Noise and Xtra Low Noise versions
Compressor suction valve (1 per refrigerant circuit)
Anti vibration mounts
Hydraulic connection sleeves
Free contacts relay card
LON gateway
Bacnet over IP Gateway
Phases control relay
Soft start
Power & Energy counter
External sensor
Condenser insulation

## Slide 54
Power counter
Power counter
Available values on
CONNECT 2 controller
Voltage on each phase (V)
Current (A)
Electrical power input (kW)
Electrical consumption (kWh)
Reduction of the electrical consumption of the unit according to maximum value

## Slide 55
Soft start
Electronic device which allows to reduce the starting current on each compressor
LG 1200V
Starting current
Direct on line
480 A
With Soft Start
352 A
-25%

## Slide 56
Phases control relay
Phases rotation direction
no phase
under and over voltage control
Relay mounted on the main power supply of the unit for the surveillance of the electricity network and safety of the unit
Asymmetry of phases

## Slide 57
RANGE
DESIGN
EFFICIENCY-COMPETITIVENESS
RUNNING LIMIT
SOUND LEVEL
ACCESSIBILITY-HYDRAULIC
CONTROL
OPTIONS
LGN serial
AGENDA

## Slide 58
Compliance :
To European regulations
Quality :
Design and manufacture as per ISO 9000-14000 quality management system
Guaranty :
Performances certified EUROVENT
Quality

## Slide 59
All
applications
-12°C / +18°C
Heat pump
operation
up to +55°C
3 acoustic
design
STD-LN-XLN
High efficiency
ESEER > 6
Compactness
Easy maintenance
11 sizes
220 à 700 kW
250 à 820 kW